## Slide 1: Autonomous Vehicle Cybersecurity PRANEETH VARMA
Tech Lead, Automotive Product Cybersecurity

## Slide 2
Autonomous Vehicle - SAE Automation Levels
Ref: https://www.nhtsa.gov/technology-innovation/automated-vehicles-safety

## Slide 3
Autonomous Vehicle - Threats
RSU
vPKI
Camera
TCU
OBU
ADAS
OBU
Camera
Radar
LiDAR
TCU
GW
OEM backend
OBD
USB
GNSS
Cellular (4G/5G)
Cloud
Cloud
Infrastructure
Smartphone
Ultrasonic
GPS
IMU
CD/DVD
Service Station
Cloud
AV Threats:
-Compromising AV off-board(Bluetooth, Wifi, V2X, MQTT, Cloud, GPS, Mobile, IT Backend etc.) and on-board (CAN, LIN,Ethernet etc,) network security
-Exploiting AV supply chain vulnerabilities
-Remotely disabling AV fleets
-AV ramming attack
-Keyless relay theaft
-Disrupting or misleading AV perception sensors(light beams, adversarial)
Powertrain
BCM
Chasis and Safety

## Slide 4
Autonomous Vehicle - Vulnerabilities
RSU
vPKI
TCU
OBU
ADAS
OBU
Camera
Radar
LiDAR
TCU
GW
OEM backend
OBD
USB
GNSS
Cellular (4G/5G)
Cloud
Cloud
Infrastructure
Smartphone
Ultrasonic
GNSS
IMU
CD/DVD
Service Station
Cloud
1.Bus (Legacy bus systems eg. CAN/LIN..lacks Authentication and Encryption, which could lead malicious Command Injection
2.Improper Access separation.
3.Unauthenticated ECU boot cycle or vulnerabilities in secure boot
4.Storage of crypto keys in clear text and unsecured location, Usage of insecure default or common keys across devices. Usage of non-side channel resistant chipsets
5.Vulnerability\weaknesses disclosed in the Bluetooth(CarBlues), Wi-Fi (KRACK vulnerability on WPA2) standard/implementations/configurations
6.Insecure configurations in offboard communication of TLS, MQTT etc.
7.Information exposure, Protection mechanism failure, Improper restriction of operations within bounds of a memory buffer, Improper input validation, NULL pointer dereference
8.Cloud security issues: misconfigured s3 buckets, EBS snapshots available to public, S3 and NS subdomain takeover, IAM issues, Insecure Lamda, lack of DDoS protection, Misconfigured AWS Cognito, SSRF, Lack of logging, Poorly configured security groups
Powertrain
BCM
Chasis and Safety

## Slide 5
Autonomous Vehicle - Risks
RSU
vPKI
TCU
OBU
ADAS
OBU
Camera
Radar
LiDAR
TCU
GW
OEM backend
OBD
USB
GNSS
Cellular (4G/5G)
Cloud
Cloud
Infrastructure
Smartphone
Ultrasonic
GPS
IMU
CD/DVD
Service Station
Cloud
1.Acceleration, braking, steering changes
2.Theaft of vehicle or its contents
3.Loss of PII linked and linkable (location tracking, contact list, VIN etc)
4.Eavesdropping on occupants
5.Insurance or lease fraud
6.Engine off or degradation
7.Driver distraction (volume, wipers, windows open and close, lights on/off etc)
8.Physical crime against the occupants

## Slide 6
Autonomous Vehicle - Countermeasures
RSU
vPKI
TCU
OBU
ADAS
OBU
Camera
Radar
LiDAR
TCU
GW
OEM backend
OBD
USB
GNSS
Cellular (4G/5G)
Cloud
Cloud
Infrastructure
Smartphone
Ultrasonic
GPS
IMU
CD/DVD
Service Station
Cloud
1.Cloud security measures: Private S3 buckets, Takedown EBS snapshot and rotate credentials, remove ns pointer, Logging and monitoring IAM activities, 2FA, remove inactive users
2.Defend from Adversarial attacks with Adversarial training, Ensemble Adversarial learning, denoising technique
3.Redundant sensors, Heuristic/ML/AI based solution for attack detection,Sensor calibration data tamper protection
3.Network security with Secure Communication:IPsec, (D)TLS, SecOC, MACsec
4,Secure Boot, Secure Update, Secure Diagnostics, Secure logging, Secure Execution, SIEM at OEM backend, Secure product lifecycle management, Secure key life cycle management, Vulnerability-incident-event management, Secure PKI
5.Encryption of external memory storage, Lock or disable debug interface, Secure storage of crypto material. Usage of side channel resistant MCU
6.Secure communication from sensors -authentication and /or encryption
7.Disabling of Auto-run capability and running of unsigned code with USB or CD/DVD player by default
8.Segregate safety critical ECU from Infotainment ECU with firewall and ID(P)S implemented at Gateway ECU
9.Implementation of proper authentication and authorization for Bluetooth and WiFi networks with least privileges, turn-off when not in use, calibrate to necessary range.Use WPA3 network encryption for WiFi.
10.High risk applications to be executed from Container/Virtualization
11.Use receiver that tracks multiple GNSS signals(GPS, GLONASS, Galileo) or Anti-spoof GPS
Powertrain
BCM
Chasis and Safety

## Slide 7
Autonomous Vehicle - Implementation Challenges
Mechanism | Layer | Description | Challenges
SecOC, UDS Service 0x27, UDS Service 0x29, DoIP | Layers 5-6-7 | Autosar SecOC: Standard from AUTOSAR, computes CMAC or signature to the I-PDU -Freshness management by appending timer (or) counter | SecOC: To perform TARA and derive the critical signals for protection UDS 0x27 and 0x29: Symmetric or Asymmetric UDS security approach to be chosen
TLS, DTLS | Transport Layer 4 | -End to End Security -Collection of protocols: Handshake, Change Cipherspec, Alert, Application data | Generation and sharing of client and server certificates, Configuring cipher suites, Selection of TLS library with light weight and secure from open-souce vulnerabilities
IPsec | Network Layer 3 | -Encrypts IP payload of any kind TCP, UDP, ICMP etc. -Collection of protocols: AH, ESP, IKE -Can not protect DHCP and ARP traffic | Complex and suitable for offboard communications
MACsec | Data link Layer 2 | -MACsec (IEEE 802.1AE) can protect all DHCP and ARP traffic -MACsec is point-to-point security protocol providing data confidentiality, integrity, replay protection and origin authenticity for traffic over layer 1 or layer 2 links of ethernet LANs -MACsec built in encryption and decryption combined with key authentication for additional security at layer 2, provided at cost effective with silicon vendor point of view | Triggers a change in silicon or a necessity for external ethernet extension card
Ethernet link | Physical Layer 1 | 1000 Base TX, 100 Base T1, 1000 Base T1, Multi-Gig | -Plausibility checks & Redundant communication -Change in design with respect to GW, Tools, Design to replace legacy networks operated on CAN

## Slide 8
Autonomous Vehicle - Security Attributes & Countermeasures
Data origin authenticity
Integrity
Controlled access (authorization)
Freshness
Non repudiation
Privacy/anonymity
Confidentiality
Availability
Controller Authentication - for confidential information
Encrypted Communication -
SecOC - for authentic signal based communication
Gateway Firewalls
TLS/DTLS
IPsec
Packet filtering
Device Authentication - authentication of client and server, data integrity
VLAN/IPSec
Security Attributes
Countermeasures
Challenges
AI/ML security
vPKI for V2X security
IDPS is difficult to be realised with AVs!
IDS needs thorough validation & verification before deployment in AVs!
Event Logging and reporting
Incident management
End of life destruction of keys
Functional Safety and Cybersecurity reconciliation & concepts implementation
……..more

## Slide 9
Autonomous Vehicle - Security
Thank you